## Slide 1
PROJECT BACKGROUND
Coal and Open-pit surface mining impacts on American Lands Follow-On (COAL-FO) is the successor project to the 2016-2017 COAL project. COAL initially aimed to deliver a suite of algorithms to identify, classify, characterize, and quantify (by reporting a number of key metrics) the direct and indirect impacts of mining operations and related destructive surface mining activities across the continental U.S (and further afield). COAL successfully delivered a Python library for processing hyperspectral imagery from remote sensing devices such as the Airborne Visible/InfraRed Imaging Spectrometer (AVIRIS) and a Science Data System for running COAL pipelines.
COAL-FO:
CS 28
COAL and Open-pit surface mining impacts on American Lands Follow-On
AVIRIS: Airborne Visible / Infrared Imaging Spectrometer
AVIRIS has been flown on four aircraft platforms: NASA's ER-2 jet, Twin Otter International's turboprop, Scaled Composites' Proteus, and NASA's WB-57.
Project Description: The COAL-FO is a continuation of a previous project completed in the 2016-2017 capstone COAL project. The COAL project was a stable python toolkit providing examples, tests, packages, stable release and stable API that identified, classified, and quantified the effects of open-pit mining on the surrounding environment. The COAL-FO project improved the existing algorithms and general functionality as well as enabled the toolkit to work with more spectral libraries.
The Mineral Classification API provides methods for generating visible-light (Figure 1)
The Mineral Classification API provides methods for mineral classified (Figure 2) images.
The Mining Identification API filters mineral classified images to identify specific classes of interest (figure 3)
The Environmental Correlation API finds pixels in a mining classified image that are within a certain number of meters from features in a vector layer (Figure 4)
Spectra: Wavelength values that vary over a range of reflectance.
Bryce has improved QGIS/GDAL installation instructions to work with more systems, created a Command Line Interface(CLI), upgraded pycoal to use USGS Spectral Library Version 7 and found more data for pycoal to classify. Kenny has worked on exporting product imagery to AWS and creating a classifier callback.
Figure 7: RGB Visible Light Image
Figure 8: USGS Spectral Library Version 6 Mineral Classification
Figure 5: AVIRIS Flight
COAL-FO will allow researchers to analyze the mineral, mining and environmental impacts to American lands from Open-pit surface mining.
Figure 9: USGS Spectral Library Version 7 Mineral Classification
The COAL project used USGS Spectral Library Version 6. The COAL-FO capstone project has designed a method for convolving USGS Spectral Library Version 7 into envi file format. This allows pycoal to classify more spectra, improving the classification images. USGS Spectral Library Version 7 is the most up to date Spectral Library by USGS and contains more spectra than any other current spectral library.
Conclusion & Results
THE TEAM:
-Lewis John Mcgibbney -Client lewis.mcgibbney@gmail.com
-Kenneth Thompson
-Student
thomkenn@oregonstate.edu
-Bryce Egley -Student egleyb@oregonstate.edu